## Slide 1: Hardware CWE™ Special Interest Group (SIG)
Steve Christey Coley, MITRE
August 2021

## Slide 2: Agenda
New CWE 4.5 / CAPEC 3.5 Released
Status Update: Top-N List
New Submissions from Paul Wortman
Reverse Engineering and CWE Scope
Update: Counterfeit / Anti-Tamper Coverage

## Slide 3: Housekeeping
Schedule:
  Next Meeting – Friday, September 3
    12:30 – 1:30 PM EST
    Microsoft Teams
Contact: cwe@mitre.org
Minutes from previous meetings available on our Github site:
  https://github.com/CWE-CAPEC/hw-cwe-sig

## Slide 4: New CAPEC 3.5 Release - June
New Supply Chain entries
  CAPEC-669: Alteration of a Software Update
  CAPEC-670: Software Development Tools Maliciously Altered
  CAPEC-671: Requirements for ASIC Functionality Maliciously Altered
  CAPEC-672: Malicious Code Implanted During Chip Programming
  CAPEC-673: Developer Signing Maliciously Altered Software
  CAPEC-674: Design for FPGA Maliciously Altered
  CAPEC-675: Retrieve Data from Decommissioned Devices
More supply chain work in the coming months

## Slide 5: New CWE 4.5 Release - July
CWE-1351: Improper Handling of Hardware Behavior in Exceptionally Cold Environments
Update to CWE-1256: Hardware Features Enable Physical Attacks from Software
  Thanks to Tortuga Logic
To do: Figure out the “right” way to support images

## Slide 6: Top-N List: Timeline to Publication
Publish 2021 HW CWE Top 10
– October –
Analysis & Development
Preliminary Top-N Survey
– April –
Send Out Final Top-10 Survey
– September –
Analyze initial responses
Refine & Iterate
Engage social & behavioral science support for survey improvement / validation
Coincide with CWE 4.6 minor release

## Slide 7: Hardware Top-N List
Goal: conduct survey in September, release in October
Consulted internal MITRE survey experts
  Great feedback on limiting to the right audience
    Hardware SIG members and other invited people with relevant roles/experience
  Operationally not feasible for MITRE to run a survey by September
Several options (decision needed ASAP)
  MITRE-led “Card-Sorting” exercise
    Performed during the SIG call or in separate meetings
  Survey operated by SIG members
Basic question: how “scientific” do we want this to be?

## Slide 8: Submissions from Paul Wortman
Many are related to less well-developed parts of CWE
HCWE102: Untrusted Manufacturing of Intellectual Property (IP)
  This may become the hardware component of a more general CWE encompassing both hardware and software. It might fall under CWE-684 (Incorrect Provision of Specified Functionality).
    CWE-684 is currently software-focused
    Might need a new entry and/or modify CWE-684
HCWE103: Verifiable Integration Testing
  We believe this should be added to CWE-684 (Incorrect Provision of Specified Functionality) as a mitigation and/or detection method
  “Testing” is not a separate element within CWE; basically treated as a detection method
  Testing seems more important for hardware

## Slide 9: Submissions from Paul Wortman (2)
HCWE105: Hardware Trojans
  This may fall under CWE-912 (Hidden Functionality), which is (or will be?) a child of CWE-684
HCWE106: Lack of Hardware Design Verification Against a Golden Standard
  “one lacks a golden standard/reference for hardware design and therefore is unable to perform the necessary validation of a final product. Post manufacturing verification is not possible without this reference material.”
  We believe this may be related to CWE-1059 (Incomplete Documentation) which in turn leads to CWE-684 or CWE-573 (Improper Following of Specification by Caller)
  Consider “Incomplete Specification” (whatever “specification” means)

## Slide 10: Proposed for Discussion
CWE-684 (Incorrect Provision of Specified Functionality)
HCWE102: (Untrusted Manufacturing of Intellectual Property (IP))
HCWE103: (Verifiable Integration Testing)
HCWE106: Golden Standard
We believe this may be related to CWE-1059 (Incomplete Documentation). CWE-1059 leads to CWE-684 or CWE-573 (Improper Following of Specification by Caller)
CWE-1059: (Incomplete Documentation)
Chain: CanPrecede
ParentOf
ParentOf
ParentOf

## Slide 11: Reverse Engineering and CWE Scope
HCWE104: Missing protective measures for preventing or hindering reverse engineering of IP or other sensitive data
  “Protections and measures intended to prevent or hinder reverse engineering of Intellectual Property (IP) are not present in the product design. These include efforts taken to prevent extraction of a product's netlist or obfuscation of hardware to protect SoC design.”
Paul has done some research (not yet public)
MITRE and Hardware SIG will need to make a decision about whether (or how) to include reverse engineering
  New CWE entries?
  “Stretch” existing entries? e.g., CWE-200
  New/existing CAPECs? e.g., CAPEC-188: Reverse Engineering

## Slide 12: Pros and Cons: Anti-Reverse Engineering
Some Pros:
  Important to manufacturers (e.g., intellectual property / theft)
  Hardware devices are deployed into untrusted environments without physical control
Some Cons:
  “Security through obscurity” - reverse engineering is a process/action that can make it easier to find weaknesses (CWE-656: Reliance on Security Through Obscurity)
  Not necessarily useful to customers
  You wouldn’t give a CVE to a leak of source code
We want to discuss this over the next month and come to a decision

## Slide 13: Update: Counterfeit / Anti-Tamper
MITRE to review proposal from SAE G32 CPSS (Joe Jarzombek @ Synopsys)
  Challenges in supply chain, Enumerating indicators of non-conformant hardware
  Proposed additions could expand CWE-1195 (Manufacturing and Life Cycle Management Concerns)
Create list of issues about scope and review with SIG (possibly a Supply Chain subcommittee)
  MITRE request submissions for weaknesses that are clearly in scope
(Sub)Community writes/adapts submissions
Relationship to supply chain
Share / collaborate with CAPEC team

## Slide 14: Next Meeting (September 3)
Topics of interest?
Questions, Requests to present? Please let us know
CWE@MITRE.ORG